## Slide 1: Introduction to Segment Routing
Standard: RFC 8402
LEONIR HOXHA
Senior Network Consultant
CISCO
CCIE #49534

## Slide 2: Agenda
Todays Challenges
Segment Routing overview & building blocks
  Prefix SID
  Adjacency SID
Topology Independent LFA (aka: Ti-LFA)
Segment Routing Traffic Engineering
  PCE Controller
Use Cases
  FlexAlgo, SDWAN over SR, Disjointness with SR-PCE, and Inter-AS with BGP Peering SID

## Slide 3: Service Creation Challenges
Complex End-to-End service provisioning:
Service stitching
Manual Operations
Heterogeneous Underlay and Overlay networks

## Slide 4: Unified “Fabric” for Service Creation
Unified underlay and overlay networks with Segment Routing and EVPN
E2E cross-domain automation with model-driven programmability and streaming telemetry

## Slide 5: Network Transport Evolution
Unified MPLS
IGP/SR
BGP-EVPN
IP
SR
Enabled Transport

## Slide 6: Segment Routing overview and Building Blocks

## Slide 7: Segment Routing
The source chooses a path and encodes it in the packet header as an ordered list of segments
Segment: is an identifier for any type of instruction
  I.e. ”Go to Node N using the shortest path”

## Slide 8: Segment Routing – Forwarding & Control Plane
MPLS: an ordered list of segments is represented as a stack of labels
IPv6: an ordered list of segments is encoded in a routing extension header
IGP distributes following Segment ID’s (SID)
  Prefix Segment (Node SID or Anycast SID)
  Adjacency Segment
A
B
C
16002
16001
16003
24001
24002
24001
24001

## Slide 9: Segment Routing – Prefix Segment ID
Shortest-path to the IGP prefix
  Equal Cost MultiPath (ECMP)-aware
Global Segment (global significance)
Label: 16000 – 24000 (default SRGB)
Statically assigned
Distributed by ISIS/OSPF
1
2
3
4
5
16005
16005
16005
16005
16005
16005
16005
1.1.1.5/32
All nodes use default SRGB 16,000 – 23,999
16004
1
2
3
4
5
16004
16004
16004
16004
16004
16004
1.1.1.4/32

## Slide 10: Segment Routing – Adjacency Segment ID
Forward to IGP adjacent Node
Local Segment (local significance)
Advertised as label value
Dynamically assigned
Distributed by ISIS/OSPF
1
2
3
4
5
24042
24045
Adj to 5
Adj to 2
24043
Adj to 3

## Slide 11: Segment Routing – Combined SIDs
Steer traffic on any path through the network
Path is specified by a stack of labels
No path is signaled
No per-flow state is created
Single protocol: IS-IS or OSPF
1
2
3
4
5
16004
24045
16004
24045
Packet to 5
24045
Packet to 5

## Slide 12: Topology Independent LFA (Ti-LFA)

## Slide 13: Topology Independent LFA (Ti-LFA)
100%-coverage 50-msec link and node protection
Simple to operate and understand
  automatically computed by the IGP
Prevents transient congestion and suboptimal routing
  leverages the post-convergence path, planned to carry the traffic

## Slide 14: Topology Independent LFA (Ti-LFA)
TI-LFA for link R1R2 on R1
Calculate P and Q spaces
Calculate post-convergence SPT
Find Q and adjacent P node on post-convergence SPT
R1 will push the prefix-SID of R4 and the adj-SID of R4-R3 link on the backup path
P-space
Q-space
1000
Packet to Z
prefix-SID(Z)
Packet to Z
Packet to Z
prefix-SID(Z)
adj-SID(R4-R3)
prefix-SID(R4)
Packet to Z
prefix-SID(Z)
adj-SID(R4-R3)
Default metric: 10
R5
R2
R1
A
Z
R3
R4
R3
R4
Packet to Z

## Slide 15: Segment Routing Traffic Engineering

## Slide 16: Traditional MPLS/RSVP-TE
Link information Distribution
  ISIS-TE
  OSPF-TE
Path Calculation
Path Setup
Forwarding Traffic down path
  Auto-route
  Static route
  PBR
  Forwarding Adjacency
  Pseudowire Tunnel select
IP/MPLS
Head end
Mid-point
Tail end
TE LSP

## Slide 17: Segment Routing Traffic Engineering
Binding Segment is a fundamental building block of SRTE
The Binding Segment is a local segment
  Has local significance
A Binding-Segment ID identifies a SRTE Policy
  Each SRTE Policy has one Binding-SID associated
Packet received with Binding-SID as top label is steered into the SRTE Policy associated with the Binding-SID
  Binding-SID label is popped, SRTE Policy’s SID list is pushed
Binding SID can be automatically assigned or statically configured as part of the SRTE policy

## Slide 18: SR-PCE Controller
PCE maintains topology and path database (established paths)
PCE specifies path as list of segment ids
PCC forwards traffic by pushing segment id list on packets
No path signaling required
Minimal forwarding state
The state is no longer in the network but in the packet
Enables centralized path initiation and update control
PCEP
SR-PCE
TED
LSP DB
PCC
Application
Path Request
Segment List:
10,20,30

## Slide 19: Feeding SR-PCE with LSP-DB
An external PCE requires some form of topology acquisition.
A PCE may learn topology using BGP-LS, IGP.
BGP-LS characteristics
  aggregates topology across one or more domains
  provides familiar operational model
New BGP-LS attribute TLVs for SR
  IGP: links, nodes, prefixes
  BGP: peer node, peer adjacency, peer set
Domain 1
Domain 2
Domain 0
BGP-LS
TED
BGP-LS
BGP-LS
RR
SR-PCE

## Slide 20: Some Use Cases with SR: - Flexible Algorithm (FlexAlgo) - SD-WAN over Segment Routing - Disjointness with SR-PCE - Inter AS with SR-PCE

## Slide 21: Multi-Plane Network with FlexAlgo
7
0
2
6
3
8
1
4
5
9
16009 Algo 0
16809 Flex-Algo 128
16909 Flex-Algo 129
Loopback 1.1.1.9/32
All the nodes support Algo 0: minimize IGP metric
Green nodes also support 128: minimize IGP metric
Red nodes also support 129: minimize Delay

## Slide 22: Multi-Plane Network with FlexAlgo
7
0
2
6
3
8
1
4
5
9
16009 Algo 0
16809 Flex-Algo 128
16909 Flex-Algo 129
Loopback 1.1.1.9/32
16009
Payload
Path to Node 9 across Algo 0

## Slide 23: Multi-Plane Network with FlexAlgo
7
0
2
6
3
8
1
4
5
9
16809
Payload
16009 Algo 0
16809 Flex-Algo 128
16909 Flex-Algo 129
Loopback 1.1.1.9/32
Path to Node 9 across Flex-Algo 128

## Slide 24: Multi-Plane Network with FlexAlgo
7
0
2
6
3
8
1
4
5
9
16909
Payload
16009 Algo 0
16809 Flex-Algo 128
16909 Flex-Algo 129
Loopback 1.1.1.9/32
Path to Node 9 across Flex-Algo 129

## Slide 25: SD-WAN over Segment Routing
SDWAN and SR integration enables a service provider to offer underlay transport SLAs for Software-Defined WAN (SDWAN) customers
The customer marks the packets with their desired QoS and transport treatment
The service provider leverages Per-Flow SR Policy to provide the underlay transport SLAs according to the customer’s marking
  Delay Sensitive traffic
  Secure and Encrypted traffic forwarding (MACsec enabled end-to-end path)
  Etc..

## Slide 26: Disjointness with SR-PCE
SID-list: {30102, 30203}
SID-list: {16007, 16008}
1
2
6
7
5
7
I:100
Default IGP link metric: I:10
I:100
3
8
4
I:100
I:100
PCE
Two dynamic paths between two different pairs (head-end, tail-end) must be disjoint from each other

## Slide 27: Inter-AS with SR-PCE & BGP Peering SID
“Pop and Forward to the BGP peer”
BGP Peering SID – like an adjacency SID external to the IGP
  Dynamically allocated but persistent
10
11
1
AS1
AS6
6
6.1.1.6/32
3
4
2
5
30024
pkt
30024
18006
16002
pkt
30024
18006
pkt
18006
pkt

## Slide 28: Conclusion
Strong customer adoption
De-facto SDN Architecture
IETF Standardization (RFC 8402)
Multi-vendor Consensus

## Slide 29: Thank You