## Slide 1: Latest Developments in SPRING (Segment Routing)
Sebastian Graf
Notes: Checking the IETF SPRING Working Group we currently see
10 active internet drafts
5 RFCs
96 related internet drafts
we take a look at two of them

## Slide 2: SPRING Introduction
This talks build upon
  “Next-Generation Traffic Engineering with SPRING” by me @DENOG8
    https://media.ccc.de/v/denog16-4008-next_generation_traffic_engineering_with_spring
  “Traffic Engineering SR/SPRING Networks using open source tools” by Tobias Heister @DENOG10
    https://media.ccc.de/v/denog10-9-traffic-engineering-sr-spring-networks-using-open-source-tools
  the talk from Leonir that you saw a minute ago
Just in order to avoid confusion:
  SPRING and Segment Routing are referring to the same concept
    SPRING is the name of the IETF working group
    Segment Routing is commonly used to describe the technology
We are going to take a look at two SPRING topics that currently have high attention
  Flex-Algo
  War of dataplane encapsulations

## Slide 3: Segment Routing with MPLS dataplane in one slide
Any path can be expressed using a combination of IGP prefix (node) segments and adjacency segments at the ingress Router
Penultimate Hop Popping may already pop Labels depending on configuration (implicit vs. explicit-null)

## Slide 4: Default IGP SPF
IGPs like OSPF and ISIS use Dijkstra Algorithm for shortest path selection (aka as shortest path first (SPF))
After SPF calculation, each node builds a directed graph with itself as root of the tree
  typically interface capacity is used as link metric using static configuration or by means of a reference bandwidth
  unused links are pruned resulting in a loop-free topology
Core
100G
100G
100G
10G
R1
R2
R3
R4
R1
R2
R3
R4
R3
R1
R4
R2
SPF from perspective of R1
SPF from perspective of R3
Notes: Dijstrka can described it in a handfull of rules (5)
unused links are pruned from the topology
R3 - R4 link never used besides for backup

## Slide 5: Issues with default SPF
With default SPF, each node only takes interface bandwidth into consideration
There might be situations where this is not desirable
Options to change this behavior include
  change IGP metric to reflect desired behavior (hammer)
    typically not possible to get desired behavior for all flows
  use a signaling protocol like RSVP to signal paths differing from IGP metric with constraints (scalpel executed locally by ingress node)
    introduces signaling overhead in the network
  using a centralized controller that tells the node how traffic should be forwarded (remotely controlled scalpel)
    adds complexity by introducing an external authority. Network falls back to SPF upon controller failure
100G
100G
100G
10G
R1
R2
R3
R4
Core

## Slide 6: Introducing Flex-Algo
Flex-Algo allows to attach multiple metrics to the same link
  might be based on delay but can be based on arbitrary values
  no additional neighbor adjacencies, just additional information shared using the LSDB
  Each node can be part of multiple Algos (signaled by LSDB)
    SPF is executed for each Algo separately
    Traffic may be steered based on requirements or SLAs
Core
100G
100G
100G
10G
R1
R2
R3
R4
10ms
10ms
10ms
1ms
R3
R4
R1
R2
R3
R1
R4
R2
Blue SPF from perspective of R3
Red SPF from perspective of R3
Notes: use different SIDs for each topology

## Slide 7: Flex-Algo in Action
Segment Routing operation with Flex-Algo is quite similar to vanilla Segment Routing
Each node advertises a node SID along with an index
  adjacency SIDs are also created for each Algo
  upon getting a labeled packet, a transit node can detect the Algo that should be used for forwarding
Algo numbers are used to identify topologies
  0 is used for the default SPF Algo
  128 to 255 can be used by operators to define different behaviors (if your vendor let’s you do that)
100G
100G
100G
10G
R1
R2
R3
R4
10ms
10ms
10ms
1ms
SID 1001
SID 4001
SID 1002
SID 4002
SID 1004
SID 4004
SID 1003
SID 4003
Core
Notes: currently two values defined:
0 – default SPF
1 – default SPF enforced (no changes allowed on downstream nodes)

## Slide 8: Flex-Algo summary
Allows distributed calculation of multiple algorithms
Not relying on central intelligence which can be an advantage or disadvantage depending on your specific situation
No additional signaling overhead introduced and automatic rerouting (if all required nodes are part of the topology)
Currently a draft in version 04
  https://datatracker.ietf.org/doc/draft-ietf-lsr-flex-algo/
Interop Demo on MPLS Congress 2019 in Paris with ISIS as IGP
  Juniper MX480, MX204
  Cisco NCS 5500, ASR9k
Notes: Other possibilities
- consider only a subset of routers
keep traffic on macsec links
keep traffic in country

## Slide 9: SPRING
War of Dataplane encapsulations

## Slide 10: Segment Routing Dataplane with MPLS
From day one SPRING defined 2 dataplane encapsulations for forwarding packets : MPLS and IPv6
MPLS was a logical choice as one option as it did not require any change to dataplane operations compared to ”classical” MPLS
  Encapsulation still based on RFC 3032 - MPLS Label Stack Encoding (2001)
  Note: Exp has been renamed to Traffic Class (TC) by RFC 5462 in 2009
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ Label
| Label | Exp |S| TTL | Stack
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ Entry
Label: Label Value, 20 bits
Exp: Experimental Use, 3 bits
S: Bottom of Stack, 1 bit
TTL: Time to Live, 8 bits
Notes: many MPLS networks out there allowed quick adoption
RFC3032 has been updated multiple times, but the encapsulation is still the same which is important as ASIC development takes time

## Slide 11: Segment Routing Dataplane with IPv6 (SRv6)
SRv6 uses IPv6 packet instead if MPLS labels which is useful for networks that do not run MPLS
  allows transit nodes that are totally unaware of SRv6
Basic mechanics are similar as with MPLS based SR, but SRv6 SIDs are not popped
  Segments Left field is used to determine the active segment
Uses 128 Bit field as SID
  split into locator / function parts
Based on Routing header defined in RFC 8200 4.4
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Next Header | Hdr Ext Len | Routing Type | Segments Left |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Last Entry | Flags | Tag |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| Segment List[0] (128 bits IPv6 address) |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| |
...
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| Segment List[n] (128 bits IPv6 address) |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
// //
// Optional Type Length Value objects (variable) //
// //
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
draft-ietf-6man-segment-routing-header-26
RFC8200
Notes: in SRv6 the entire Stack of SIDs stays in the packet
Next-Header = 43 for Routing Header
Flags = 8 bit unused for future use
tag = classify packet as part of a group
Routing Type = 4 (Segment Routing Header)
Optional TLV = padding or HMAC (Hashed Message Authentication Code)

## Slide 12: SRv6 Dataplane in action – 1/4
Let’s see how this looks on the dataplane
  R1 is SRv6 capable and wants to send a packet to R6
  the packet should use R5 as intermediate hop
  we are assuming equal IGP costs on all links
Traffic Class
Version
Flow Label
Payload Length
Next Header = 43
Hop Limit
Source Address = 1::
Destination Address = 3::
Next Header
Length
Type = 4
Segments Left = 2
Last Entry
Flags
Tag
Segment List [0] = 6::
Segment List [1] = 5::
Segment List [2] = 3::
Payload
R1
SID 1::
R2
non-SRv6
R3
SID 3::
R4
SID 4::
R6
SID 6::
R5
SID 5::
R7
SID 7::
IPv6
SA = 1:: DA = 3::
SRv6
SL = 2 [6::, 5::, 3::]
Notes: we use quite shortened SIDs for readability

## Slide 13: SRv6 Dataplane in action – 2/4
The packets reaches R2 which is not SRv6 capable
R2 performs standard forwarding based on the IPv6 destination address
No changes are been done in the SRv6 Header when the packet is forwarded towards R3
IPv6
SA = 1:: DA = 3::
SRv6
SL = 2 [6::, 5::, 3::]
R1
SID 1::
R2
non-SRv6
R3
SID 3::
R4
SID 4::
R6
SID 6::
R5
SID 5::
R7
SID 7::

## Slide 14: SRv6 Dataplane in action – 3/4
The packets reaches R3 which is SRv6 capable
R3 evaluates the SRv6 header once it recognizes that the IPv6 destination address is equal to it’s own IPv6 address
  check if the “segments left” field is > 0
    decrease by one
    copy the new active segment into the destination address field from the IPv6 header
    the new active segment is the one towards R5
IPv6
SA = 1:: DA = 5::
SRv6
SL = 1 [6::, 5::, 3::]
IPv6
SA = 1:: DA = 3::
SRv6
SL = 2 [6::, 5::, 3::]
R1
SID 1::
R2
non-SRv6
R3
SID 3::
R4
SID 4::
R6
SID 6::
R5
SID 5::
R7
SID 7::

## Slide 15: SRv6 Dataplane in action – 4/4
The packets reaches R5 which is SRv6 capable
R5 evaluates the SRv6 header once it recognizes that the IPv6 destination address is equal to it’s own IPv6 address
  check if the “segments left” field is > 0
    decrease by one
    copy the new active segment into the destination address field from the IPv6 header
    the new active segment is the one towards R6
R7 forwards the frame based on the destination address. No SRv6 processing is done
R6 recognizes it’s own IP as destination address
  as the “segments left” field is 0, R6 knows that the final destination has been reached for the SR-path
IPv6
SA = 1:: DA = 6::
SRv6
SL = 0 [6::, 5::, 3::]
R1
SID 1::
R2
non-SRv6
R3
SID 3::
R4
SID 4::
R6
SID 6::
R5
SID 5::
R7
SID 7::
IPv6
SA = 1:: DA = 5::
SRv6
SL = 1 [6::, 5::, 3::]

## Slide 16: IPv6 SIDs in detail
A SRv6 SID is consisting of a locator part and a function
The locator part uniquely identifies a node within a SRv6 network, while the function identifies a specific service on that node
The operator is free to choose the length of the locator. Whatever bits are left used going to identify the function
From draft-ietf-lsr-isis-srv6-extensions:
    Locators associated with Flexible Algorithms SHOULD NOT be advertised in Prefix Reachability TLVs (236 or 237)
    Locators associated with algorithm 0 (for all supported topologies) SHOULD be advertised in a Prefix Reachability TLV (236 or 237) so that legacy routers (i.e., routers which do NOT support SRv6) will install a forwarding entry for algorithm 0 SRv6 traffic
    SRv6 SIDs are not directly routable and MUST NOT be installed in the forwarding plane. Reachability to SRv6 SIDs depends upon the existence of a covering locator
2001:db8:3333:4444:5555:6666
7777:8888
:
Locator
Function
Notes: SRv6 SIDs have a structure which is different to SIDs with MPLS Dataplane
Now that we have seen SIDs with SRv6 are these IPv6 Addresses or not?
Function could also contains arguments

## Slide 17: SRv6 – watch the overhead
Using 128 bit SIDs creates more overhead as with MPLS
  Number of required SIDs depend on the actual application. Here some examples with some explicit hops
  with 3 SRv6 SIDs our original packet of 576 Bytes grows to 672 Bytes (17% increase) => 14% total overhead
  with 8 SRv6 SIDs our original packet of 576 Bytes grows to 744 Bytes (29% increase) => 23% total overhead
    note that SRv6 could use fewer SIDs to achieve the same result as it can combine transport and function in one SID
Same calculation with MPLS
  with 3 MPLS labels our original packet of 576 Bytes grows to 588 Bytes (2% increase) => 2% total overhead
  with 8 MPLS labels our original packet of 576 Bytes grows to 608 Bytes (6% increase) => 5% total overhead
IPv6
IPv6
IPv6
SRv6
576
576
40
8 + N * 16
IPv6
IPv6
MPLS
576
576
N * 4
Notes: Besides overhead : consider lookup bandwidth of ASICs
- MPLS only needs to process the top label, SRv6 needs to complete stack
Simple Example: MPLS overhead 8 Bytes, SRv6 64 Bytes

## Slide 18: Alternatives to reduce overhead with SRv6
Compressed Routing Header - draft-bonica-6man-comp-rtg-hdr
  uses 16 or 32 bit SIDs (CRH-16, CRH-32) and shortened header
  sometimes referred to as SRv6+
  CRH must end on 64-bit boundary
SRoUDP - draft-ietf-mpls-sr-over-ip-03
  encapsulates into IPv4 or IPv6 packets with UDP header (calculation on the right uses IPv6)
  32 bits SIDs after UDP header
Technology | Packet size w/ 3 SIDs | Packet size w/ 8 SIDs
MPLS | 588 (+2%, total 2%) | 608 (+6%, total 5%)
CRH-16 | 632 (+10%, total 9%) | 640 (+11%, total 10%)
CRH-32 | 632 (+10%, total 9%) | 656 (+14%, total 12%)
SRoUDP (IPv6) | 636 (+10%, total 9%) | 656 (+14%, total 12%)
SRv6 | 672 (+17%, total 14%) | 744 (+29%, total 23%)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Next Header | Hdr Ext Len | Routing Type | Segments Left |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
+ SID[0] +
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
+ SID[1] +
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
// //
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
+ SID[n] +
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
CRH-32
Notes: CRH gets rid of last_entry, flags, SIDs and optional TLVs

## Slide 19: Conclusion
SPRING is still a hot topic and there is a lot of development
FlexAlgo implementations are available / about to be released from vendors
Watch out who wins the war of dataplane encapsulations